## Slide 1
EUR Tenant ACI Redesign
From 11 VRFs / 266 EPGs to 2 VRFs / 39 EPGs with ESG-Ready Segmentation
Strategy & Migration Process
Consolidate routing · Adopt descriptive naming · Introduce ESGs · Preserve every IP
Project: terraform-esg / aci-redesign | Tenant: EUR | Schema: AEDCE
Prepared from IPv4_REDESIGN_OVERVIEW.md and aci-redesign/README.md

## Slide 2
Agenda
What this deck covers and the order we walk through it
1 Why redesign
Problems with today's 11-VRF / 266-EPG layout
2 Target architecture
2 VRFs, 39 BDs/EPGs, ESGs, vzAny
3 Key design decisions
Why 2 VRFs, why L2 'DMZ' stays in VRF-EUR, no IP changes
4 BD consolidation
How 215 legacy BDs map into 39 functional BDs
5 Naming & object model
Descriptive naming conventions
6 Phased security model
vzAny → single ESG → zone ESGs → tight contracts
7 Lab migration (greenfield)
4 phases - build from scratch
8 Production migration (brownfield)
7 phases - live coexistence
9 VMM / VLAN strategy
Dynamic VLAN pool 3501-3967, vmm-vcenter-rcc
10 Risks & mitigations
Where traffic loss can happen and how we contain it
11 What gets deployed
Concrete object list from Terraform apply
12 Decommission plan
30 legacy BDs to remove
13 Deployment architecture
How YAML becomes ACI config via nac-aci + MCP sidecar
14 Automation design decisions
Four non-obvious choices that protect the pipeline
15 Secrets strategy
Env → CI → Vault progression, same TF_VAR_* names
16 Local developer workflow
What an operator actually types
17 CI/CD pipeline
GitLab stages: validate → plan → deploy → destroy
18 Operations & troubleshooting
auth-check, diagnose, common failure modes
19 Next steps
What to do after this deck
ACI Redesign Strategy
2 / 27

## Slide 3
Executive Summary
One-page view of the redesign and why it matters
The Goal
• Collapse 11 legacy VRFs into 2 routing domains: VRF-EUR (internal) and VRF-DMZ (proxy).
• Replace 215 numeric bridge domains and 266 EPGs with 39 descriptive, function-named BDs/EPGs that match the IPv6 RCC model.
• Introduce Endpoint Security Groups (ESGs) so segmentation can be enforced by policy instead of by VRF routing isolation.
• Keep every existing IPv4 subnet and gateway address in place - no host, VM, or switch is readdressed.
• Start permissive (vzAny permit-all) and tighten progressively using ESGs and targeted contracts.
Why now
• 11-VRF model added operational complexity without meaningful security (firewall already enforces real boundaries).
• Numeric naming (BD-V0372, EPG-V0572) hides function and slows incident response.
• No ESGs means no realistic path to micro-segmentation at scale.
11 → 2
VRFs
215 → 39
Bridge Domains
266 → 39
EPGs
13 → ~4
L3Outs (prod)
0
IP Address Changes
2
New ESGs (Phase 2)
ACI Redesign Strategy
3 / 27

## Slide 4
Current State - What's Deployed Today
EUR tenant / AEDCE schema in production APIC
Attribute | Value
Tenant | EUR
Schema | AEDCE
VRFs (11) | EUR-E, EUR-AIS, EUR-AIM, EUR-AIV, EUR-AIZ, EUR-AIG, EUR-AIP, EUR-AOV-UC-DMZ, EUR-ARMY-ENT-SVR-DMZ, EUR-GSN-Test, EUR-E catch-all
Bridge Domains | 215 (numeric: BD-V0005 → BD-V2205)
EPGs | 266 (numeric: EPG-V0005 → EPG-V2205)
Contracts | Per-VRF individual contracts (no vzAny)
ESGs | None
L3Outs | 13
VMM Domain | VMM1
Problems With the Current Design
• VRFs created for segmentation, but the firewall already enforces real security boundaries.
• Numeric BD/EPG names hide function - operators must cross-reference alias tables.
• 266 EPGs are hard to audit, contract, and change.
• No ESGs = no realistic path to micro-segmentation.
• L3Out sprawl (13) complicates routing and changes.
Takeaway: the fabric works, but its object model fights operators every day. A flatter, name-driven model closes the gap without touching a single IP address.
ACI Redesign Strategy
4 / 27

## Slide 5
Target State - 2-VRF Redesign
VRF-EUR + VRF-DMZ, 39 BDs, 39 EPGs, 2 ESGs, vzAny permit-all start
Attribute | Target
Tenant | EUR (unchanged)
VRFs | 2 - VRF-EUR (internal) + VRF-DMZ (proxy segments)
Bridge Domains | 39 descriptive - BD-AD, BD-APP-SVR, BD-CFG-MGMT, ...
EPGs | 39 (1:1 with BDs) - EPG-AD, EPG-APP-SVR, ...
Contracts | vzAny permit-all (initial) - tightened via ESGs later
ESGs | ESG-All-Internal-EPGs (36) + ESG-All-DMZ-EPGs (3) - deferred (nac-ndo ~> 1.2.0 lacks ESG selectors)
App Profiles | AppProf-NetCentric, AppProf-DMZ
IPv6 (VRF-RCC) | Unchanged - managed separately in ndo-terraform-nac
Why this shape
• VRF-EUR consolidates all internal IPv4 traffic into a single routing domain.
• VRF-DMZ keeps proxy segments (139.139.x.x) routing-isolated from internal.
• vzAny makes initial cut-over safe and reversible.
• ESGs give a classification layer today and a policy layer tomorrow.
Subnet consolidation across the 215 legacy BDs
22
BDs carrying real IPv4 subnets (110 subnets total)
17
Placeholder BDs (IPv6-only categories)
14
L2-only BDs (gateway on firewall)
30
Decommission (20 dead + 4 deprecated + 6 test)
ACI Redesign Strategy
5 / 27

## Slide 6
Target Architecture Diagram
Tenant EUR - two VRFs, vzAny per VRF, ESGs grouping all EPGs
Tenant: EUR
Filters: Any | Contracts: Any_VRF-EUR, Any_VRF-DMZ
VRF-EUR - Internal IPv4 | vzAny: Any_VRF-EUR (permit-all)
36 Bridge Domains (22 with IPv4 subnets · 14 placeholders)
BD-AD
BD-APP-SVR (32)
BD-CFG-MGMT (19)
BD-WEB-SVR (11)
BD-DB-SVR (8)
BD-VVOIP-MGMT (9)
BD-MECM (6)
BD-BACKUP-SVR (4)
BD-FILE-SVR (3)
BD-SYSLOG (3)
BD-LB (3)
BD-ACAS-SCANNERS (2)
BD-NMS
BD-PATCH
BD-PKI-SRV
BD-VHOST-MGMT
BD-VVOIP-PROXY
BD-ADM-DCO
BD-DNS-MGMT (L2)
BD-GEF-MGMT (L2)
BD-ACAS-MGMT*
BD-ADFS*
BD-C2C-SCANNERS*
BD-DHCP-SVR*
BD-E911-SVR*
BD-FMWR-SVR*
BD-LMR*
BD-NAC*
BD-OCSP*
BD-PRINT-SVR*
BD-RCC-DCO*
BD-RCC-DNS*
BD-RCC-SVR*
BD-RCC-UNIX*
BD-SMTP-SVR*
BD-SYSMAN*
* placeholder BD - created for parity with IPv6 RCC model, no IPv4 subnet yet
AppProf-NetCentric
• 36 EPGs (EPG-AD, EPG-APP-SVR, ...)
• Bound to VMM domain vmm-vcenter-rcc
• Dynamic VLAN 3501-3967
ESG-All-Internal-EPGs
• Selects all 36 internal EPGs
• Provider + consumer of Any_VRF-EUR
• Classification ready for Phase 3
VRF-DMZ - Proxy
BD-D64-PROXY*
BD-FWEB-PROXY (3)
BD-RWEB-PROXY*
AppProf-DMZ
• 3 EPGs on vmm-vcenter-rcc
• Dynamic VLAN 3501-3967
ESG-All-DMZ-EPGs
• Selects all 3 DMZ EPGs
• Provider + consumer of Any_VRF-DMZ
ACI Redesign Strategy
6 / 27

## Slide 7
Key Design Decisions
Why the target model looks the way it does
Decision | Rationale
2 VRFs instead of 11 | The firewall already enforces real security boundaries - extra VRFs added ops complexity without security value. ESGs + contracts replace VRF-based segmentation.
VRF-EUR (internal) | Consolidates EUR-E (101) + EUR-AIS (132) + EUR-AIM (15) + EUR-AIV (12) + EUR-AIZ (11) + EUR-AIG (1) + EUR-AIP (4) + EUR-GSN-Test (1) ≈ 276 legacy EPGs.
VRF-DMZ | Keeps EUR-AOV-UC-DMZ and EUR-ARMY-ENT-SVR-DMZ routing-isolated - DMZ must never share a routing table with internal.
VRF-RCC (IPv6) | Unchanged. Managed separately in ndo-terraform-nac/136.215.4.96/. No IPv6 refactor in this redesign.
Descriptive naming | BD-DNS-MGMT / EPG-DNS-MGMT replace numeric BD-V0005 / EPG-V0005. Same conventions as the IPv6 RCC model.
vzAny permit-all (initial) | All EPGs can talk inside a VRF on day 1. ESGs classify endpoints today so contracts can be tightened tomorrow without reclassification.
L3Out consolidation | Production shrinks 13 L3Outs to ~4 (1 internal + 1 DMZ per site). Lab does not deploy L3Outs.
L2 'DMZ'-aliased BDs stay in VRF-EUR | Gateway lives on an external firewall - VRF choice doesn't affect routing. ESG-based grouping (Phase 3) enforces the DMZ/internal boundary instead.
ACI Redesign Strategy
7 / 27

## Slide 8
Brownfield-Safe: No IP Addresses Change
Every existing subnet is preserved under the new naming structure
Example - BD-APP-SVR (VRF-EUR) absorbs 32 subnets
155.155.236.65/26
was BD-V0572 / APCE_EUR_APPS
155.155.172.1/24
was BD-V0372 / APCG_EUR_APPS
155.155.108.1/24
was BD-V0272 / APCK_EUR_APPS
136.215.37.129/26
was BD-V0455 / APCK_RDS
…
28 more subnets absorbed under BD-APP-SVR
What actually moves
• Gateway MAC/IP stays on ACI - assigned to a renamed BD.
• EPG identifiers change, but endpoint IPs don't.
• BDs may carry multiple anycast subnets (one BD, many old BDs).
• VMM rebinding is transparent - VDS port groups are refreshed by ACI.
Why this de-risks the migration
• No DNS, firewall, or NAT changes required.
• Hosts/VMs/switches don't get new addresses.
• Per-subnet change windows - not a big-bang migration.
• Rollback is a VRF reassignment, not a readdressing project.
ACI Redesign Strategy
8 / 27

## Slide 9
BD Consolidation - 215 Legacy → 39 Functional
Every legacy BD is accounted for (mapped, placeholder, or decommissioned)
New BD | Subnets | Legacy BDs absorbed | Primary function
BD-APP-SVR | 32 subnets | 39 legacy BDs | Application servers, VDI, ITSM apps
BD-CFG-MGMT | 19 subnets | 40 legacy BDs | Server mgmt (OOB, inband, DRAC, IACS)
BD-WEB-SVR | 11 subnets | 18 legacy BDs | Web frontends, ITSM web tiers
BD-VVOIP-MGMT | 9 subnets | 14 legacy BDs | UC public/restricted, gateways, messaging
BD-DB-SVR | 8 subnets | 11 legacy BDs | SQL / database backends
BD-MECM | 6 subnets | 6 legacy BDs | SCCM / MECM patching infrastructure
BD-BACKUP-SVR | 4 subnets | — | Backup infrastructure
BD-FILE-SVR / BD-SYSLOG / BD-LB | 3 subnets each | — | File services, logging, load balancers
171 legacy BDs
legacy BDs mapped with subnets (110 subnets across 22 new BDs)
14 legacy BDs
L2-only (function known, gateway on firewall)
17 legacy BDs
Placeholder BDs (IPv6-only categories)
30 legacy BDs
Decommission candidates (20 dead + 4 deprecated + 6 test)
ACI Redesign Strategy
9 / 27

## Slide 10
Naming & Object Model
Production-ready conventions aligned with the IPv6 RCC model
Object | Pattern | Example
VRF (internal) | VRF-EUR | VRF-EUR
VRF (DMZ) | VRF-DMZ | VRF-DMZ
VRF (IPv6) | VRF-RCC (unchanged) | VRF-RCC
Contract | Any_<VRF> | Any_VRF-EUR, Any_VRF-DMZ
Filter | Any (ethertype unspecified) | Any
Bridge Domain | BD-<function> | BD-DNS-MGMT, BD-UC-DMZ
EPG | EPG-<function> | EPG-DNS-MGMT, EPG-UC-DMZ
App Profile (internal) | AppProf-NetCentric | AppProf-NetCentric
App Profile (DMZ) | AppProf-DMZ | AppProf-DMZ
App Profile (ESGs) | AppProf-SecurityGroups | AppProf-SecurityGroups
ESG (internal) | ESG-All-Internal-EPGs | ESG-All-Internal-EPGs
ESG (DMZ) | ESG-All-DMZ-EPGs | ESG-All-DMZ-EPGs
Legacy → Redesign
• BD-V0172 / V0222 / V0322 → BD-AD
• BD-V0372 + 38 more → BD-APP-SVR
• BD-V0016 + 39 more → BD-CFG-MGMT
• BD-V0250 + 10 more → BD-DB-SVR
•
• Each new BD inherits every IPv4 subnet from the legacy BDs it replaces (per docs/reports/bd_mapping_analysis.txt).
ACI Redesign Strategy
10 / 27

## Slide 11
Phased Security Model
Start permissive, add classification, then tighten - without breaking anyone
Phase 1
vzAny permit-all on VRF-EUR + VRF-DMZ
Open - any EPG in a VRF can talk
Current
Phase 2
Single ESG per VRF grouping all EPGs
Classification ready, no policy change yet
Current
Phase 3
Split ESGs by zone (ESG-AIM, ESG-AIS, ESG-DMZ-Apps, ...)
Segmentation by function with inter-ESG contracts
Future
Phase 4
Tighten contracts to required flows only
Micro-segmentation
Future
Why phased?
• Phase 1+2 deliver the new object model with zero behavior change.
• Phases 3-4 add enforcement, one zone / one contract at a time.
• Every phase is independently reversible; no phase requires an IP change.
ACI Redesign Strategy
11 / 27

## Slide 12
Lab Migration (Greenfield)
Built from scratch to validate the target design
Phase | Name | What | Status
1 | Base build | 2 VRFs, 39 BDs with consolidated IPv4 subnets, 39 EPGs, VMM domain, vzAny | ✓ Complete
2 | ESG grouping | 36 internal + 3 DMZ EPGs grouped under ESG-All-Internal-EPGs and ESG-All-DMZ-EPGs | ✓ Complete
3 | Zone ESGs | Split into ESG-AIM, ESG-AIS, ESG-DMZ-Apps, ... with inter-ESG contracts | Future
4 | Contract tightening | Restrict flows to what apps actually need | Future
How the lab runs
• make init / plan / apply from aci-redesign/apic-vmware/.
• nac-aci module (v0.7.0) consumes YAML in data/nac-aci-shared/ + data/nac-aci-aedcg/.
• Local state file; first apply creates ~200+ ACI objects.
• Validation: APIC GUI + vCenter port group presence.
Lab tooling
• apic-vmware/main.tf - nac-aci module wiring
• data/nac-aci-aedcg/access-policies.nac.yaml - VLAN pool + AAEP (per-fabric)
• data/nac-aci-aedcg-rendered/vmm-domain.nac.yaml - rendered from TF_VAR_vcenter_* (gitignored)
• data/nac-aci-shared/tenant-epg-nac.nac.yaml - 2 VRFs, 39 BDs/EPGs, ESGs (cross-fabric)
ACI Redesign Strategy
12 / 27

## Slide 13
Production Migration (Brownfield)
Coexistence model - live traffic keeps flowing through every phase
Phase | Action | Key consideration
1 | Create VRF-EUR and VRF-DMZ alongside existing 11 VRFs | None - new VRFs are empty
2 | Create new BDs with descriptive names in VRF-EUR/VRF-DMZ | None - new BDs have no endpoints yet
3 | Create ESGs and vzAny contracts on VRF-EUR/VRF-DMZ | None - policy ready, no enforcement yet
4 | Migrate EPGs one-at-a-time from old VRFs to new VRFs | Brief traffic loss per subnet - schedule maintenance windows
5 | Consolidate L3Outs (13 → ~4) | Routing re-convergence - coordinate with FW/WAN teams
6 | Rename EPGs/BDs from numeric to descriptive | Cosmetic only - can be done during or after
7 | Decommission old VRFs, contracts, and L3Outs | None (once all EPGs migrated and validated)
Phase 4 is the critical step
Moving a BD from one VRF to another causes endpoint re-learning (~seconds of traffic loss per subnet). Each subnet gets its own change window. Plan with app teams.
ACI Redesign Strategy
13 / 27

## Slide 14
Risks & Mitigations
Where traffic loss can occur and how we contain it
Risk | Impact | Mitigation | Level
BD VRF reassignment (Phase 4) | Endpoint re-learning on the BD - brief L2/L3 blip per subnet. | Per-subnet change windows · notify app teams · rollback = reverse VRF reassignment | HIGH
L3Out consolidation (Phase 5) | Routing re-convergence at the fabric boundary. | Coordinate with firewall/WAN teams · phased cutover · route monitoring during change | HIGH
VMM VDS rebinding | Port group updates in vCenter as EPGs move between VMM-bound BDs. | Use read-write VMM domain · validate in lab first · schedule outside peak hours | MED
Contract tightening (Phase 3-4) | Flows that weren't designed for can break. | Log-first mode · use ESGs to group before tightening · staged contract rollout | MED
Naming / alias drift | Legacy scripts referencing numeric EPG names break. | Keep aliases during Phase 6 · rename with deprecation notice · update automation | LOW
Decommission timing | Removing old VRFs/L3Outs before all EPGs migrate. | Gate decom on validation checklist per subnet · automated orphan object report | LOW
ACI Redesign Strategy
14 / 27

## Slide 15
VMM & VLAN Strategy
Dynamic VLAN assignment under the new VMM domain
VLAN allocation plan
3001-3500
3501-3967
3968-4095
IPv6 RCC EPGs (static)
VMM domain (IPv4 EPGs, dynamic)
ACI reserved (do not use)
Component | Configuration
VMM domain | vmm-vcenter-rcc (lab) / VMM1 (production)
vCenter controller | vcenter01 with credential policy
Virtual Distributed Switch | Created by ACI via dvs_version (6.5 / 6.6 / 7.0 / 8.0)
AAEP | vmm-aaep - linked to VMM domain
Port channel policy | mac-pinning
Uplinks | uplink1, uplink2
Leaf interface profile | leaf-152-153-intprof (ports 1-48, AEDCG nodes 152-153)
Production config touch-points
• data/sites/primary/access_policies.nac.yaml - VLAN pool VMM1 = 3501-3967, AAEP infra_vlan, VPC-VMM-HOSTS.
• data/sites/primary/fabric_policies.nac.yaml - VMM1 read-write, tag collection, mac-pinning, uplinks, dvs_version.
• data/ndo/schema_AEDCE.nac.yaml - all 405 EPG site entries bound to VMM1 (dynamic VLAN, immediate deployment).
• Replace CHANGE_ME placeholders with real vCenter IP / DC / creds before apply.
ACI Redesign Strategy
15 / 27

## Slide 16
What Gets Deployed
Concrete ACI objects created by terraform apply
Access & Fabric Policies
Object | Detail
VLAN pool | vmm-vlan-pool (dynamic, 3501-3967)
CDP / LLDP / LACP | cdp-enabled, lldp-enabled, lacp-active
Port channel | mac-pinning
Link level | 10G
VMware VMM domain | vmm-vcenter-rcc (read-write, manages VDS)
vCenter controller | vcenter01 with credential policy
VDS uplinks | uplink1, uplink2
AAEP | vmm-aaep - linked to VMM domain
VPC interface policy group | vpc-vmm-hosts
Leaf interface profile | AEDCG: leaf-152-153-intprof / AEDCK: leaf-119-191-intprof
Leaf switch profile | AEDCG: leaf-152-153-prof (152-153) / AEDCK: leaf-119-191-prof (119, 191)
Tenant EUR
Object | Detail
Filter | Any (ethertype unspecified)
Contract | Any_VRF-EUR (scope: context)
Contract | Any_VRF-DMZ (scope: context)
VRF-EUR | vzAny provider + consumer of Any_VRF-EUR
VRF-DMZ | vzAny provider + consumer of Any_VRF-DMZ
Bridge Domains (internal) | 36 BDs - multi-subnet from legacy consolidation
Bridge Domains (DMZ) | 3 BDs - BD-D64-PROXY, BD-FWEB-PROXY, BD-RWEB-PROXY
App Profile - NetCentric | 36 internal EPGs on vmm-vcenter-rcc (dynamic VLAN)
App Profile - DMZ | 3 DMZ EPGs on vmm-vcenter-rcc (dynamic VLAN)
App Profile - SecurityGroups | ESG-All-Internal-EPGs, ESG-All-DMZ-EPGs
ACI Redesign Strategy
16 / 27

## Slide 17
Decommission Plan
30 legacy BDs removed during or after migration
Dead / empty (20)
• BD-2250
• BD-V0005
• BD-V0006
• BD-V0958
• BD-V0970
• BD-V1116
• BD-V1117
• BD-V1120
• BD-V1140 … BD-V1149
• BD-V1571
• BD-V2150
Deprecated (4)
• BD-V0009 (Native VLAN)
• BD-V0021 (ATM - 'may need to remove')
• BD-V0529 ('Remove' in alias)
• BD-GSN-Test
Temporary test (6)
• BD-V0020
• BD-V2001
• BD-V2002
• BD-V2003
• BD-V2004
• BD-V2005
• (all TMP_SATTest)
Decommission guardrails
• Only remove after every EPG from an old VRF has migrated and been validated.
• Run an orphan-object report (no endpoints, no contracts, no L3Out references) before delete.
• Keep an auditable record of each removal - terraform state + APIC audit log.
ACI Redesign Strategy
17 / 27

## Slide 18
What Changes vs What Stays the Same
Quick sanity check before we start
Aspect | Changes | Stays the same
IP addresses | — | All subnets preserved, no readdressing
VRF count | 11 → 2 | —
BD / EPG count | 215 / 266 → 39 / 39 | —
BD / EPG names | Numeric → descriptive | —
Contracts | Per-EPG → vzAny + ESG | Contract model (still ACI contracts)
VMM domain | VMM1 → vmm-vcenter-rcc (lab) | Dynamic VLAN assignment
L3Outs | 13 → ~4 (production) | External routing concept
Firewall | — | Still enforces DMZ boundaries
IPv6 (VRF-RCC) | — | Unchanged, managed separately
The redesign rewrites the object model, not the network.
ACI Redesign Strategy
18 / 27

## Slide 19
Deployment Architecture
How YAML intent becomes ACI configuration
Inputs (source-controlled YAML)
• data/nac-aci-shared/ - cross-fabric tenant (VRFs, BDs, EPGs, ESGs, contracts)
• data/nac-aci-aedcg/ - per-fabric access policies (AEDCG)
• data/nac-aci-aedcg-rendered/ - vmm-domain YAML (gitignored)
• templates/vmm-domain.nac.yaml.tftpl - template for the above
• terraform.tfvars - non-sensitive only (apic_url, username)
Terraform (orchestration)
• module "aci" - netascode/nac-aci@0.7.0 (wrapper)
• reads all YAML files from the two yaml_directories
• aci_mcp sub-module DISABLED via modules.nac.yaml
• module "aci_mcp" - standalone, owns MCP Instance Policy
• receives sensitive var.mcp_key from env/CI/Vault
• provider "aci" - CiscoDevNet/aci ≥ 2.0.0
APIC (enforcement)
• ~200+ objects: VRFs, BDs, EPGs, ESGs, contracts, filters
• AppProf-NetCentric / AppProf-DMZ / AppProf-SecurityGroups
• VMM domain vmm-vcenter-rcc + dynamic VLAN pool 3501-3967
• MCP Instance Policy (mcpInstP-default) with compliant key
• Access policies: AAEP, domain profile, interface selectors
Pre-step: scripts/render-vmm-yaml.sh (orchestrated by Makefile / CI)
Substitutes TF_VAR_vcenter_* env vars into the template and writes the rendered VMM YAML into the gitignored data/nac-aci-aedcg-rendered/ directory BEFORE terraform plan runs. Decoupling the render from Terraform is what lets nac-aci evaluate its for_each/count at plan time.
ACI Redesign Strategy
19 / 27

## Slide 20
Design Decisions (Automation Layer)
Four non-obvious choices; each protects the pipeline from a specific failure mode
Decision | Problem it solves | How we implemented it
1. aci_mcp sub-module is disabled in the nac-aci wrapper | nac-aci unconditionally creates the MCP Instance Policy with a hard-coded default key of 'cisco', which APIC 5.2+/6.x rejects with Error 182. | Disable via modules.nac.yaml (modules.aci_mcp: false). Own the MCP policy directly in main.tf with a sensitive var.mcp_key sourced from env/CI/Vault.
2. VMM YAML is rendered by a shell script, not a local_file resource | A module with depends_on on an un-applied resource defers every internal for_each/count to apply-time. Result: terraform plan fails with a wall of "Invalid count argument" errors. | Render the template in scripts/render-vmm-yaml.sh BEFORE terraform runs. The rendered YAML is a static input at plan time, so nac-aci's graph evaluates cleanly.
3. Secrets are NOT declared in terraform.tfvars | Terraform variable precedence: values in terraform.tfvars beat TF_VAR_* env vars. Leaving an empty slot silently overrides the env var and breaks auth. | Leave apic_password and mcp_key undeclared in tfvars entirely. The env var / CI variable / Vault data source always wins.
4. vCenter values are NOT Terraform variables | Putting the vCenter service-account password into a Terraform variable puts it into state and plan output, even marked sensitive. | Consume them directly in render-vmm-yaml.sh. They never become TF variables, never enter state, never appear in plan output. Rotation = re-export + re-plan.
If any of these four are "fixed" back to the obvious shape, the pipeline breaks. Full rationale: aci-redesign/README.md → Design Decisions.
ACI Redesign Strategy
20 / 27

## Slide 21
Secrets Strategy: Env → CI → Vault
Same Terraform code; the source of secrets evolves with maturity
Stage 1: Local Dev
Shell environment variables
source scripts/set-apic-password.sh
eval "$(./scripts/generate-mcp-key.sh)"
export TF_VAR_vcenter_username='...'
export TF_VAR_vcenter_password='...'
make auth-check → HTTP 200
make plan / make apply
Stage 2: GitLab CI
Masked + Protected CI variables
Settings → CI/CD → Variables:
APIC_PASSWORD (masked, protected)
MCP_KEY (masked, protected)
VCENTER_USERNAME (masked, protected)
VCENTER_PASSWORD (masked, protected)
VCENTER_HOSTNAME_IP (plain)
VCENTER_DATACENTER (plain)
VCENTER_DVS_VERSION (plain)
.gitlab-ci.yml maps each to TF_VAR_*.
Stage 3: Vault
Centralized KV store (AppRole for runners)
data "vault_kv_secret_v2" "aci_lab" {
mount = "secret"
name = "aci/lab"
}
Wrapper pulls secrets into TF_VAR_* env
at pipeline start. No Terraform code change.
Same lab/prod parity, centralized audit.
The 7 TF_VAR_* names never change. Only the producer changes: shell → CI → Vault.
ACI Redesign Strategy
21 / 27

## Slide 22
Local Developer Workflow
What an operator actually types, start to finish
1
Enter the project
cd aci-redesign/apic-vmware
2
Export APIC password (hidden prompt, one per shell)
source scripts/set-apic-password.sh
3
Export strong MCP key
eval "$(./scripts/generate-mcp-key.sh)"
4
Export vCenter values
export TF_VAR_vcenter_hostname_ip='198.18.134.80'
export TF_VAR_vcenter_datacenter='Datacenter'
export TF_VAR_vcenter_username='administrator@vsphere.local'
export TF_VAR_vcenter_password='<single-quoted>'
export TF_VAR_vcenter_dvs_version='6.6'
5
Prove credentials before touching state
make auth-check # must print HTTP 200
6
Plan and apply
make plan # renders VMM YAML + terraform plan
make apply # re-renders + applies plan.tfplan
Why each step matters
• Steps 1-4 populate the 7 TF_VAR_* the Makefile checks.
• Step 5 isolates credential bugs from Terraform bugs.
• Steps 6 renders YAML + runs terraform; make fails fast if any TF_VAR_* is unset.
Env vars don't survive a new terminal
• Every new shell repeats steps 2-4.
• Use one terminal per session to avoid drift.
• set-apic-password.sh must be sourced, not executed.
First-time machine setup
• make init once per checkout (downloads providers).
• Details: aci-redesign/README.md → Getting Started.
ACI Redesign Strategy
22 / 27

## Slide 23
CI/CD Pipeline (GitLab)
Four stages; same TF_VAR_* names as local dev, sourced from masked CI variables
validate
on every push
• ci-secret-scan.sh (fails pipeline on plaintext secrets)
• render-vmm-yaml.sh
• terraform fmt -check -recursive
• terraform init -backend=false
• terraform validate
plan
on every push
• render-vmm-yaml.sh
• terraform init + terraform plan -out=plan.tfplan
• Artifact: plan.tfplan (30 days)
• Needs all 7 TF_VAR_* masked CI variables
deploy
manual gate
• terraform apply plan.tfplan
• Runs only when a reviewer clicks the play button
• Same TF_VAR_* as plan; no surprise credentials
destroy
manual gate
• terraform plan -destroy + terraform apply
• Never auto-triggered
• Used for tearing down lab experiments cleanly
GitLab CI variable → TF_VAR_* mapping
APIC_PASSWORD → TF_VAR_apic_password · MCP_KEY → TF_VAR_mcp_key · VCENTER_HOSTNAME_IP → TF_VAR_vcenter_hostname_ip · VCENTER_DATACENTER → TF_VAR_vcenter_datacenter · VCENTER_USERNAME → TF_VAR_vcenter_username · VCENTER_PASSWORD → TF_VAR_vcenter_password · VCENTER_DVS_VERSION → TF_VAR_vcenter_dvs_version
ACI Redesign Strategy
23 / 27

## Slide 24
Operations & Troubleshooting
Small toolset; each command answers one specific question
make auth-check → interpret the HTTP code
HTTP 200
OK
Credentials accepted. Proceed with make plan.
HTTP 401
Bad credentials
APIC rejected username/password. Re-source set-apic-password.sh; run diagnose-apic-auth.sh to compare env-var password vs freshly-typed.
HTTP 403
Account locked
Too many failures. Wait 5-10 min, or unlock via another admin (APIC → Admin → AAA → Security → Users).
HTTP 000
No response
APIC unreachable / TLS failure / wrong URL. Test: curl -k https://<apic>/api/aaaLogin.json
Command reference
• make auth-check credential probe (no terraform)
• ./scripts/diagnose-apic-auth.sh env-var vs typed comparison
• source scripts/set-apic-password.sh refresh stale password
• make render re-generate VMM YAML only
• make plan / apply normal change cycle
• make destroy tear everything down
• make clean wipe plan + rendered YAML
Failure modes & fix
• terraform plan shows "Invalid count" → rendered VMM YAML missing; run make render.
• "Authentication details not provided" → TF_VAR_apic_password unset; source set-apic-password.sh.
• APIC 401 even after re-export → you exported in a DIFFERENT shell than the one running make. Same terminal only.
• "Password is required for MCP Instance Policy" → TF_VAR_mcp_key missing or < 8 chars; regenerate with generate-mcp-key.sh.
• CI secret-scan failure → plaintext password committed to tracked YAML or .tfvars; remove and force-rotate the credential.
ACI Redesign Strategy
24 / 27

## Slide 25
Two-Root Architecture: APIC-direct + NDO
Each control plane drives the layer it actually owns
apic-vmware/ - APIC-direct
• Two providers via aliases: aci (AEDCG) + aci.aedck (AEDCK).
• Owns access/fabric policies (leaf profiles, AAEP, VPC).
• Owns MCP Instance Policy per fabric (sensitive key).
• Owns VMware VMM domain (vmmDomP) per fabric.
• manage_tenants = false - does NOT create tenant content.
  ◦ Why APIC-direct: leaf profiles and the VMM domain object are per-fabric and not modelable in NDO.
ndo/ - NDO-managed
• Single mso provider (platform=nd, login_domain=local).
• Owns schema AEDCE-IPv4 + template Tenant_EUR_IPv4.
• Owns 2 VRFs (vzAny), 2 contracts, 39 BDs, 2 ANPs, 39 EPGs.
• EPGs bind to vmm-vcenter-rcc on AEDCG + AEDCK.
• manage_tenants = false - EUR pre-exists in NDO.
• deploy_templates = false - operator clicks Deploy.
  ◦ Why NDO: only NDO does cross-site policy stitching for stretched BDs/EPGs across two APIC fabrics.
Cutover order (clean lab): apic-vmware/ apply -> ndo/ apply -> click Deploy in NDO UI -> scripts/deploy_bindings.py -> click Deploy again
ACI Redesign Strategy
25 / 27

## Slide 26
NDO Operator Workflow
Single-template deploy + static port bindings, end-to-end
1
Authenticate to NDO
cd aci-redesign/ndo
source scripts/set-ndo-password.sh
make auth-check # must return token
2
Apply schema (NDO only, no APIC push)
make plan && make apply
# Creates schema AEDCE-IPv4 / template Tenant_EUR_IPv4
# 2 VRFs, 2 contracts, 39 BDs, 2 ANPs, 39 EPGs in NDO
# deploy_templates=false -> nothing on APICs yet
3
Deploy from NDO UI (manual click)
Schemas -> AEDCE-IPv4 -> Tenant_EUR_IPv4 -> Deploy to sites
Review per-site preview -> Confirm
After this: tenant content lives on AEDCG + AEDCK
4
Push static port bindings
cd aci-redesign/scripts
cp bindings.example.json bindings.json && $EDITOR bindings.json
./deploy_bindings.py bindings.json --no-vault --dry-run
./deploy_bindings.py bindings.json --no-vault
5
Re-deploy in NDO UI
Static port adds sit pending -> click Deploy again
Endpoints can now be plugged in
Day-2 changes: edit data/nac-ndo/, make plan/apply, click Deploy. Schema refactor: make destroy (NDO-only; APIC untouched), edit, plan, apply, redeploy.
ACI Redesign Strategy
26 / 27

## Slide 27
Next Steps
Where this deck hands off
Lab
• Phase 1 complete: NDO schema AEDCE-IPv4 / single template Tenant_EUR_IPv4 deployed via apic-vmware/ + ndo/.
• Push static port bindings via scripts/deploy_bindings.py and re-deploy from NDO UI.
• Phase 2 (ESGs) deferred until nac-ndo exposes ESG selectors.
• Document membership rules ahead of Phase 3 (zone ESGs).
Production prep
• Review bd_mapping_analysis.txt with app/ops owners.
• Confirm L3Out target topology with firewall/WAN teams.
• Schedule per-subnet change windows for Phase 4.
• Dry-run NDO single-template apply in a non-prod schema.
Tooling / automation
• Promote ndo/ root from manual deploy_templates=false to CI-driven once the runbook is stable.
• Add orphan-object report to CI before Phase 7 (decom).
• Wire validation checks (EPG counts, BD counts, VMM bindings) into GitLab CI.
• Track placeholder BDs until their IPv4 function is confirmed.
Same network, cleaner model, safer change path.
ACI Redesign Strategy
27 / 27